### 2021 Annual Water Quality Report - Town of Dungannon PWSID #1169225

Is my water safe?

We are pleased to present this year's Annual Water Quality Report (Consumer Confidence Report) as required by the Safe Drinking Water Act (SDWA). This report is designed to provide details about where your water comes from, what it contains, and how it compares to standards set by regulatory agencies. This report is a snapshot of last year's water quality. We are committed to providing you with information because informed customers are our best allies.

Do I need to take special precautions?

Some people may be more vulnerable to contaminants in drinking water than the general population. Immuno-compromised persons such as persons with cancer undergoing chemotherapy, persons who have undergone organ transplants, people with HIV/AIDS or other immune system disorders, some elderly, and infants can be particularly at risk from infections. These people should seek advice about drinking water from their health care providers. EPA/Centers for Disease Control (CDC) guidelines on appropriate means to lessen the risk of infection by Cryptosporidium and other microbial contaminants are available from the Safe Water Drinking Hotline (800-426-4791).

Where does my water come from?

The sources of your drinking water are:

- SCPSA Duffield water treatment plant.  The source of supply is North Fork of the Clinch River.

- Town of Gate City water treatment plant.  The source of supply is Big Moccasin Creek near Gate City and Weber City.

- SCPSA’s Moccasin Gap water treatment plant. The source of supply is also Big Moccasin Creek.

- Fort Blackmore Methodist Camp Well.  This groundwater source is located near Fort Blackmore.  The well is treated by chlorination for disinfection.

Treatment is by chemical and physical means including filtration to remove particulate matter, chlorination for disinfection, and fluoridation for the promotion of dental health.

Source Water Assessment and its Availability

The Virginia Department of Health conducted a source water assessment of the river source in 2002. The North Fork of the Clinch River and the Big Moccasin Creek were determined to be of high susceptibility to contamination using the criteria developed by the state in its approved Source Water Assessment Program. The assessment report consists of maps showing the source water assessment area and an inventory of known land use activities of concern. The report is available by contacting the person listed elsewhere in this report.

Why are there contaminants in my drinking water?

Drinking water, including bottled water, may reasonably be expected to contain at least small amounts of some contaminants. The presence of contaminants does not necessarily indicate that water poses a health risk. More information about contaminants and potential health effects can be obtained by calling the Environmental Protection Agency's (EPA) Safe Drinking Water Hotline (800-426-4791). The sources of drinking water (both tap water and bottled water) include rivers, lakes, streams, ponds, reservoirs, springs, and wells. As water travels over the surface of the land or through the ground, it dissolves naturally occurring minerals and, in some cases, radioactive material, and can pick up substances resulting from the presence of animals or from human activity:

- Microbial contaminants, such as viruses and bacteria, that may come from sewage treatment plants, septic systems, agricultural livestock operations, and wildlife;

- Inorganic contaminants, such as salts and metals, which can be naturally occurring or result from urban stormwater runoff, industrial, or domestic wastewater discharges, oil and gas production, mining, or farming;

- Pesticides and herbicides, which may come from a variety of sources such as agriculture, urban stormwater runoff, and residential uses;

- Organic Chemical Contaminants, including synthetic and volatile organic chemicals, which are by-products of industrial processes and petroleum production, and can also come from gas stations, urban stormwater runoff, and septic systems;

- Radioactive contaminants, which can be naturally occurring or be the result of oil and gas production and mining activities.

In order to ensure that tap water is safe to drink, EPA prescribes regulations that limit the amount of certain contaminants in water provided by public water systems. Food and Drug Administration (FDA) regulations establish limits for contaminants in bottled water which must provide the same protection for public health.

How can I get involved?

The Town of Dungannon Council meets in the Town Hall on the 1st Monday of each month at 6:00 PM. Any changes to the monthly meeting will be posted.

Other Information - Sodium

There is presently no established standard for sodium in drinking water. Water containing more than 270 ppm of sodium should not be used as drinking water by those persons whose physician has placed them on a moderately restricted sodium diet. Water containing more than 20 ppm should not be used as drinking water by those persons whose physician has placed them on a severely restricted sodium diet. For informational purposes, we wish to point out that the results of our most recent sampling (2021) indicate that your water has a sodium content of ranging from N/D – 6.3 ppm.

Additional Information for Lead

If present, elevated levels of lead can cause serious health problems, especially for pregnant women and young children. Lead in drinking water is primarily from materials and components associated with service lines and home plumbing. Town of Dungannon is responsible for providing high quality drinking water, but cannot control the variety of materials used in plumbing components. When your water has been sitting for several hours, you can minimize the potential for lead exposure by flushing your tap for 30 seconds to 2 minutes before using water for drinking or cooking. If you are concerned about lead in your water, you may wish to have your water tested. Information on lead in drinking water, testing methods, and steps you can take to minimize exposure is available from the Safe Drinking Water Hotline or at http://www.epa.gov/safewater/lead.

Monitoring and Reporting Violations

NOTICE TO CONSUMERS

of the Town of Dungannon Waterworks

Waterworks ID No. 1169225

We have been advised by State health officials of a failure to perform required monitoring in accordance with the Commonwealth of Virginia/State Board of Health Waterworks Regulations.

We are required to monitor your drinking water for specific contaminants on a regular basis.  Results of regular monitoring are an indicator of whether or not our drinking water meets health standards.  During the month of September 2021, we did not monitor for total trihalomethanes and haloacetic acids and therefore, cannot be sure of the quality of our drinking water during that time.

State health officials feel there is little need for concern about the safety of your water because past records show that our system has had no documented problems with total trihalomethanes and haloacetic acids contamination; however, routine sampling and analysis is required to determine the quality of water delivered to our customers.

There is nothing you need to do at this time.

We plan to collect the samples for analysis during September 2022.

For more information, please contact:

Aneshia Stidham, Operator

2450 Hunters Valley East, Dungannon, VA  24245 (mailing address)

(276) 467-2373 (telephone number)

Water Quality Data Table

In order to ensure that tap water is safe to drink, EPA prescribes regulations which limit the amount of contaminants in water provided by public water systems. The table below lists all of the drinking water contaminants that we detected during the calendar year of this report. Although many more contaminants were tested, only those substances listed below were found in your water. All sources of drinking water contain some naturally occurring contaminants. At low levels, these substances are generally not harmful in our drinking water. Removing all contaminants would be extremely expensive, and in most cases, would not provide increased protection of public health. A few naturally occurring minerals may actually improve the taste of drinking water and have nutritional value at low levels. Unless otherwise noted, the data presented in this table is from testing done in the calendar year of the report. The EPA or the State requires us to monitor for certain contaminants less than once per year because the concentrations of these contaminants do not vary significantly from year to year, or the system is not considered vulnerable to this type of contamination. As such, some of our data, though representative, may be more than one year old. In this table you will find terms and abbreviations that might not be familiar to you. To help you better understand these terms, we have provided the definitions below the table.

| Contaminants | MCLG or MRDLG | MCL, TT, or MRDL | Detect In Your Water | Range | Sample Date | Violation | Typical Source |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | Low | High |  |  |  |
| Disinfectants & Disinfection By-Products |
| (There is convincing evidence that addition of a disinfectant is necessary for control of microbial contaminants) |
| Chlorine (as Cl2) (ppm) | 4 | 4 | 1.47 | 0.5 | 2.0 | 2021 | No | Water additive used to control microbes |
| Haloacetic Acids (HAA5) (ppb) | NA | 60 | 2 | NA | NA | 2021 | No | By-product of drinking water chlorination |
| TTHMs [Total Trihalomethanes] (ppb) | NA | 80 | 10 | NA | NA | 2021 | No | By-product of drinking water disinfection |
| Inorganic Contaminants |
| Barium (ppm) | 2 | 2 | 0.048 | 0.018 | 0.048 | 2021 | No | Discharge of drilling wastes; Discharge from metal refineries; Erosion of natural deposits |
| Fluoride (ppm) | 4 | 4 | 0.67 | 0.34 | 0.67 | 2021 | No | Erosion of natural deposits; Water additive which promotes strong teeth; Discharge from fertilizer and aluminum factories |
| Nitrate [measured as Nitrogen] (ppm) | 10 | 10 | 1.1 | N/D | 1.1 | 2021 | No | Runoff from fertilizer use; Leaching from septic tanks, sewage; Erosion of natural deposits |
| Sodium (optional) (ppm) | NA | NA | 6.3 | N/D | 6.3 | 2021 | No | Erosion of natural deposits; Leaching; See more information about Sodium in the “Other Information” section elsewhere in this report. |
| Microbiological Contaminants |
| Turbidity (NTU) | NA | 95% of Values < 0.3 | 100% of Values < 0.3 | 0.02 | 0.19 | 2021 | No | Soil runoff |
| 100% of the samples were below the TT value of 0.3; A TT violation occurs when less than 95% of samples measure below 0.3. The highest single measurement was 0.19. Any measurement in excess of 1.0 is a violation unless otherwise approved by the state. |
| Radioactive Contaminants |
| Alpha emitters (pCi/L) | 0 | 15 | 2.89 | N/D | 2.89 | 2018 & 2021 | No | Erosion of natural deposits |
| Radium (combined 226/228) (pCi/L) | 0 | 5 | 1.43 | ND | 1.43 | 2018 & 2021 | No | Erosion of natural deposits |

| Contaminants | MCLG | AL | Your Water | Sample Date | # Samples Exceeding AL | Exceeds AL | Typical Source |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Inorganic Contaminants |
| Copper - action level at consumer taps (ppm) | 1.3 | 1.3 | .106 | 2019 | 0 | No | Corrosion of household plumbing systems; Erosion of natural deposits |
| Lead - action level at consumer taps (ppb) | 0 | 15 | 2.76 | 2019 | 0 | No | Corrosion of household plumbing systems; Erosion of natural deposits |

| Unit Descriptions |
| --- |
| Term | Definition |
| ppm | ppm: parts per million, or milligrams per liter (mg/L) |
| ppb | ppb: parts per billion, or micrograms per liter (µg/L) |
| NTU | NTU: Nephelometric Turbidity Units. Turbidity is a measure of the cloudiness of the water. We monitor it because it is a good indicator of the effectiveness of our filtration system. |
| NA | NA: not applicable |
| ND | ND: Not detected |
| NR | NR: Monitoring not required, but recommended. |

| Important Drinking Water Definitions |
| --- |
| Term | Definition |
| MCLG | MCLG: Maximum Contaminant Level Goal: The level of a contaminant in drinking water below which there is no known or expected risk to health. MCLGs allow for a margin of safety. |
| MCL | MCL: Maximum Contaminant Level: The highest level of a contaminant that is allowed in drinking water. MCLs are set as close to the MCLGs as feasible using the best available treatment technology. |
| TT | TT: Treatment Technique: A required process intended to reduce the level of a contaminant in drinking water. |
| AL | AL: Action Level: The concentration of a contaminant which, if exceeded, triggers treatment or other requirements which a water system must follow. |
| Variances and Exemptions | Variances and Exemptions: State or EPA permission not to meet an MCL or a treatment technique under certain conditions. |
| MRDLG | MRDLG: Maximum residual disinfection level goal. The level of a drinking water disinfectant below which there is no known or expected risk to health. MRDLGs do not reflect the benefits of the use of disinfectants to control microbial contaminants. |
| MRDL | MRDL: Maximum residual disinfectant level. The highest level of a disinfectant allowed in drinking water. There is convincing evidence that addition of a disinfectant is necessary for control of microbial contaminants. |
| MNR | MNR: Monitored Not Regulated |
| MPL | MPL: State Assigned Maximum Permissible Level |

For more information please contact:

Contact Name: Mayor Debra Horne
Address: 18948 Veterans Memorial Highway/P.O. Box 278
	   Dungannon, VA 24245
Phone: 276-467-2522